## Slide 1
Railway Track Crack Detection System
Presented by :
Priyank Rathore (21DCS014)
Presented To :
Dr. Robin Singh Bhadoria
Assistant Professor
DEPARTMENT OF COMPUTER SCIENCE & ENGINEERING
NATIONAL INSTITUTE OF TECHNOLOGY HAMIRPUR

## Slide 2
Table of Contents
  Introduction
  Theoretical Background
  Proposed System
  List of Components
  System Block Diagram
  Circuit Diagram
  Working Principle
  Benefits & Limitations
  Conclusion

## Slide 3
Introduction
  Railways are one of the oldest and most used transportation systems.
  Track-related failures like cracks can cause fatal accidents.
  Railway accidents are often caused by:
    Undetected cracks or breaks in the track
    Delay in manual inspections
  These issues are more dangerous in:
    Remote areas
    Nighttime operations
  Need a smart, low-cost, real-time crack detection solution.

## Slide 4
Project Objective
  Detect cracks automatically using sensors.
  Use Arduino to control detection and communication.
  Send SMS alerts with location when a crack is found.
  Ensure continuous monitoring regardless of time or location.

## Slide 5
Theoretical Background
  Cracks are small gaps or damages on the railway track.
  If not detected early, they can lead to derailments.
  Traditional detection methods:
    Manual inspection (slow and risky)
    Expensive advanced systems
  Our system combines basic electronics and automation for smarter detection.

## Slide 6
Overview of the Proposed System
  A robotic vehicle moves on the track.
  Ultrasonic sensor continuously checks rail level.
  If a gap is found (distance > 2.5 cm):
    Car stops
    LED and buzzer activate
    GPS detects location
    GSM sends alert SMS

## Slide 7
Component | Description
Arduino UNO R3 | Controls all devices
Ultrasonic Sensor | Detects cracks
GSM SIM800L | Sends SMS alerts
GPS Module | Gets location
L298N Motor Driver | Controls DC motors
List of Components
Component | Description
DC Motors | Moves the car
LED & Buzzer | Alert indicators
3.7V Batteries | Power supply

## Slide 8
Arduino UNO R3
  A microcontroller that reads sensor data and controls devices.
  Used in DIY electronics projects.
  Can be programmed using Arduino IDE.
  In our project:
    Controls sensors, motors, buzzer, LED.
    Makes decisions based on sensor values.

## Slide 9
Ultrasonic Sensor (HC-SR04)
  Measures distance using sound waves.
  Sends a pulse and waits for it to bounce back.
  Time taken → calculates distance.
  If rail gap > threshold → assumes crack present.

## Slide 10
GPS Module
  Global Positioning System module.
  Reads current longitude and latitude.
  Helps track the exact location of the crack.
  Sends this info via GSM.

## Slide 11
Motor Driver (L298N) & DC Motors
  L298N receives control signals from Arduino.
  Controls direction and speed of 2 DC motors.
  Drives the prototype vehicle forward or stops it when a crack is found.

## Slide 12
LED & Buzzer
  LED lights up and buzzer rings when crack is detected.
  These provide immediate visual and audio alerts.

## Slide 13
Power Supply
  Two 3.7V rechargeable lithium batteries.
  Provides power to Arduino, motors, sensors.
  Batteries are lightweight and can be recharged easily.

## Slide 14
Circuit Diagram

## Slide 15
System Block Diagram

## Slide 16
Working Principle
  Car moves forward on the track.
  Sensor checks distance between rails.
  If the distance > 2.5 cm → crack detected.
  LED & buzzer turn ON, motors stop, location is sent to station.
  If distance is safe → car continues to move.

## Slide 17
Benefits & Limitations
Benefits:
  Real-time crack detection
  Low cost
  Useful day and night
  Can reduce major accidents

## Slide 18
Benefits & Limitations
Limitations:
  Sensor protection in rain/dust
  GSM signal availability
  Battery drainage
  Small prototype; needs large-scale upgrade

## Slide 19
Conclusion
  A smart way to monitor railway tracks.
  Can be implemented for better safety and less manual work.
  Future improvements:
    Solar charging
    AI-based crack pattern recognition
    Cloud-based real-time tracking

## Slide 20
References
  A. S. Prasad, S. J, P. Shandilya and G. S, "Intelligent Railway Track Crack Detection System," 2024 8th International Conference on Computational System and Information Technology for Sustainable Solutions (CSITSS), Bengaluru, India, 2024, pp. 1-5, doi: 10.1109/CSITSS64042.2024.10816777.
  Automatic Railway Gate Crossing Control and Track Crack Detection System Using IoT Y. Maheswar , J. Hemalatha , G. Surya , G. Suryanarayana Reddy , D. Bhargav (2024). https://ijatem.com/wp-content/uploads/2024/05/IJATEM-24_004.pdf
  I. Devulapalli, A. V. Vennelakanti and R. Sallakunta, "Real-Time Railway Track Fault Detection and Environmental Monitoring System Using Arduino and GSM," 2024 4th International Conference on Technological Advancements in Computational Sciences (ICTACS), Tashkent, Uzbekistan, 2024, pp. 1410-1415, doi: 10.1109/ICTACS62700.2024.10840621.

## Slide 21
THANK
YOU